## Slide 1
Problem Description: NO PANEL DISPLAY NO LIGHT ON CONTROL BUTTON | Machine Model : DIPDZ | Machine No: HD188 | Package : HZIP
1) Details of the Problem:
5) CAPA and Recommendations:
2) Containment Actions
Permanent Solutions and Recommendation
1. Machine display panel and control button malfunction after power cycle
 | What | Who | When | Remarks
1 | Check 24V power output | Drix / Eugene | 17.07,06 | Done
2 | Check 5V power output | Drix / Eugene | 17.07,06 | Insufficient power output, it measures 4.7V, trimmer for voltage adjustment is already at max
3 | Replace 5V power supply then adjust trimmer | Drix / Eugene | 17.07,06 | Done
 | What | Who | When | Remarks
1 | Replace power supply | Drix |  | done
2 |  |  |  | 
POST MORTEM
4)Pictures and Illustrations
Machine | Why1 | Why2 | Why3 | Why4 | Why5
 | Insufficient supply | Power supply component breakdown | Run to fail |  | 
Outflow | Why1 | Why2 | Why3 | Why4 | Why5
Systemic Root cause |  |  |  |  | 
 | Why1 | Why2 | Why3 | Why4 | Why5
3)Root cause analysis:
Adjust trimmer to satisfy control panel voltage requirement, adjusted to 5.6V
5V Power Supply
TDK
ESX05-6R0