## Slide 1
Problem Description: Intermittent Test Result | Machine Model:EA5204H Machine No:HD168 | Package: DIP30SD | Work Week: 32.1
1) Details of the Problem:
4) Recommendations :
2) Containment Actions/Interim Actions:
Continuous fail
 | What | Who | When | Remarks
1 | Pull-out contactor assemble revert the roller of contactor | Milo | 17.08.04 | Ok
2 | Aligned contactor with respect to device leads | Milo | 17.08.04 | OK
3 | Auto run machine and conducted leads sampling | Milo | 17.08.04 | Ok
 | What | Who | When
1 | Include in check item/check sheet | PM Group | Scheduled PM
Intermittent Test Result
3)Pictures and Illustrations
3) Root cause analysis: Worn –out roller of contactor
Machine | Why1 | Why2 | Why3 | Why4 | Why5
 | Worn-out contactor roller | No specific lifetime when to replace | Not included in PM check item | Run to fail | 
Outflow | Why1 | Why2 | Why3 | Why4 | Why5
 | No defined tool life |  |  |  | 
Systemic Root cause |  |  |  |  | 
 | Why1 | Why2 | Why3 | Why4 | Why5
Worn-out roller of contactor result to intermittent test result
Condition upon Reverting roller