## Slide 1
Problem Description: System error 124 | Machine Model : HX-8100 | Machine No:HD349 | Package : QUAD
1) Details of the Problem:
5) CAPA and Recommendations:
3) Root cause analysis: Defective actuator cylinder and loose cam follower lock nut
2) Containment Actions/Interim Actions:
Machine | Why1 | Why2 | Why3 | Why4 | Why5
 | Stacked z axis assy | unable to moved | Defective gear |  | 
Outflow | Why1 | Why2 | Why3 | Why4 | Why5
 | Undefined tool life |  |  |  | 
Systemic Root cause |  |  |  |  | 
 | Why1 | Why2 | Why3 | Why4 | Why5
Permanent Solutions and Recommendation
System error 124
 | What | Who | When | Remarks
1 | Checked handler z axis motor | Jher/pong | 17.07.19 | Ok
2 | unable to moved z axis assy | jher/pong | 17.07.19 | Done
3 | Stacked up z axis motor | Jher/pong | 17.07.19 | NG z motor
 | What | Who | When | Remarks
1 | Replaced z motor | Jher/pong | WW29 | OK
2 | Recommend checking of motors every PM schedule | PM robot |  | open
POST MORTEM
4)Pictures and Illustrations
Stacked z motor
Replaced z motor