## Slide 1
Problem Description: Frequent sf device rotation failure(2-H and 2-D) | Machine Model:RT2158 Machine No:HD364 | Package: TQFP281L | Work Week: 29.2
1) Details of the Problem:
4) Recommendations :
2) Containment Actions/Interim Actions:
Long down time due to frequent sf device rotation failure
 | What | Who | When | Remarks
1 | Conducted pin to pin checking | Milo | 17.07.16 | Ok
2 | Checked cables of sf motor unloader rotation2 | Milo | 17.07.16 | With broken wire
3 | Re-soldered broken wires | Milo | 17.07.16 | Ok
4 | Changed position of SF unloader rotation2 motor | Milo | 17.07.16 | Ok
5 | Replace Defective sensor | Pong | 17.07.16 | Ok
 | What | Who | When
1 | Include in check item/check sheet | PM Group | Scheduled PM
SF DEVICE ROTATION FAILURE(2-H&2-D)
3)Pictures and Illustrations
3) Root cause analysis: Poor alignment of sensor Holder
Machine | Why1 | Why2 | Why3 | Why4 | Why5
 | Deformed sensor holder | Untighten/Loose cap screws | No specific lifetime when to replace | Not included in PM check item | Run to fail
Outflow | Why1 | Why2 | Why3 | Why4 | Why5
 | No defined tool life |  |  |  | 
Systemic Root cause |  |  |  |  | 
 | Why1 | Why2 | Why3 | Why4 | Why5
Broken wires of motor and sensor cause during collision
Poor alignment of sensor holder result to damage
Position of motor wires facing to sensor result to damaged