## Slide 1: Machine hung-up UENO01

## Slide 2
Bios setting:
  Press up or down button, highlight advanced chipset features, then press enter to select
  Press PCI express root port function
  Change all ports settings from auto to change to disabled, highlight auto setting pressing arrow up and down, then press enter. Select disabled setting by pressing up and down, then enter
  After setting is done, press F10 to save the setting.
  Reboot mc then power on-same GPIB error
  Encounter pop-up error application(the memory could not be written)
  Restart MC then reinsert slave and master card-same GPIB error
  Machine power off, take out slave card
  Machine power on, 3 mins machine power off
  Connect slave card then power on-same
  Try to reboot without slave card then insert slave card on 40 sec. count-machine progress
  Restart machine-machine reboot
  Return to original position then run to production
  ROOT CAUSE: CF card not detected
  Recommendation: possible replacement for CF card
GBIB ERROR
PANEL FREEZE
MEMORY SLAVE AND MASTER (cf card)