## Slide 1
Problem encountered on Ueno06.
Machine Serial No. 142553-1
Machine module: Taping module

## Slide 2
423.4microns
495.7 microns
Sample 1
Sample 2
Problem: Frequent carrier tape pocket offset( backward)
Note: Already patched 400 microns compensation. But we still encountered more than 400 microns pocket offset.
Suggestion: Please make the carrier tape pocket offset up to 600 microns pocket offset as stated on the previous report.
Error encountered: PKG insertion error( jam at tape insertion ).
Risk assessment: Possible will cause of device bottom scratches and chipping on top package.
ERROR DISPLAY
TILTED DEVICE
Problem encountered on Ueno06 frequent taping offset pocket

## Slide 3
Center distance carrier tape pocket
Offset backward carrier tape pocket
Turret nozzle
Tape vision system
Insertion jam detection
Gap = 2 mm
Distance = 72 mm
Note: Folded carrier tape causing offset pocket
Findings/Root cause: Harmonic drive motor angular speed is greater than Feed2 offset motor angular speed causing folded carrier tape during carrier tape indexing resulting to frequent pocket offset.
Harmonic Drive motor = 700 pulse
Feed2 offset motor value = 500 pulse
Corrective action: Set the Feed 2 offset motor angular speed greater than Harmonic drive motor angular speed
Harmonic Drive motor = 200 pulse
Feed2 offset motor value = 500 pulse
Note: Machine set up for 3M carrier tape.
Preventive Action/s:
Review and Setup all Ueno handler taping module angular speed differences of harmonic drive and feed2 offset motors.
Set the machine capability to align the pocket offset up to 600 microns compensation.
Revise Ueno documentation included to setup and conversion procedure.
Harmonic Drive Motor
Bottom base
Problem: Tape pocket frequently dislocated backward during machine running.

## Slide 4
Carrier tape input
Carrier tape Output
Urethane clamper
Tension spring
Feed2 offset motor
Harmonic drive motor
C-curve
Tape vision system
Tape Sealing system
Good Setup: Feed2 offset motor > Harmonic drive motor
Controller Setup: Feed2 move offset > Feed2 origin offset
F2>F1
F1
F2
Turret nozzle
Taping Module good Set up